MINI SPLITTER

Thru Input    DMX Input  DC Input

DMX Output

Thank you for having chosen our AFX DMX DISTRIBUTOR. For your own safety, please read this user manual carefully before installing the device.

### SAFETY INTRODUCTION

- If the device has been exposed to temperature changes due to environmental changes, do not switch it on immediately.

The arising condensation could damage the device. Leave the device switched off until it has reached room temperature.

- It is essential that the device is earthed. A qualified person must carry out the electric connection.

- Make sure that the available voltage is not higher than stated at the end of this manual.

- Make sure the power cord is never crimped or damaged. If it is damaged, ask your dealer or authorized agent to replace the power cord.

- Always disconnect from the mains, when the device is not in use or before cleaning it. Only handle the power cord by plug.

Never pull out the plug by tugging the power cord.

- DISCONNECT DEVICE: Where the MAINS plug or an appliance coupler is used as the disconnect device, the disconnect device shall remain readily operable.

- Shields, lenses or ultraviolet screens shall be changed if they have become visibly damaged to such an extent that their effectiveness is impaired, for example by cracks or deep scratches.

### CAUTION:

- Be very careful during installation. Since you will be working with a dangerous voltage you can suffer a life-threatening electric shock when touching live wired.

- Never look directly into the light source, as sensitive persons may suffer an epileptic shock.

- Please be aware that damages caused by manual modifications to the device are not subject to warranty. Keep away from children and non-professionals.

- The light doesn’t include any spare parts for repair, please check if all the parts are well installed and screws are fitted tightly before operating. Do not use the light when the cover is open.

### GENERAL GUIDELINES

- This device is only allowed to be operated with an alternating current of max. 220-240VAC and was designed for indoor use only.

- Do not shake the device. Avoid brute force when installing or operating it.

- When choosing the installation spot, please make sure that the device is not exposed to extreme heat, moisture or dust.

The minimum distance between light-output from the projector and the illuminated surface must be more than 1 meter. Keep a distance to any flammable objects of at least 5m.

- Operate the device only after having familiarized yourself with its functions. Do not permit operation by person not

qualified for operating the device. Most damages are the result of unprofessional operation.

- Please use the original packaging if the device is to be transported.

- For safety reasons, please be aware that all modifications on the device are forbidden. Furthermore, any other operation may lead to short-circuit, burns, electric shock, lamp explosion, crash, etc. If this device will be operated in any way

different to the one described in this manual, the product may suffer damages and the guarantee becomes void.

### MOUNTING

Orientation

This fixture may be mounted in any position, provided there is adequate room for ventilation

When selecting installation location, take into consideration lamp replacement access and routine maintenance. Safety cables must always be used.

Never mount in places where the fixture will be exposed to rain, high humidity, extreme temperature changes or restricted ventilation.

If the external flexible cable or cord of this light is damaged, it shall be exclusively replaced by the manufacturer or his service agent or a similar qualified person in order to avoid a hazard.

Make sure the installation position is stable before you fix the light. When the light is reverse hanging, make sure the light will not fall from the truss, use the safety cable go through the truss and bracket of the light as a supporting, to avoid the light to fall down. There is no entrance to the work area during mounting. Periodically check if the safety cable has fretted away or clamp is loosened. We will not take any responsibility for damages caused by a badly installed unit.

### Power Supply and Signal Cable Connection

- Mains Power connection

The exclusive plug should be used between the connection of unit and power. Please ensure that the rated voltage and frequency are accordance with the power supply. The required input voltage and frequency are: 220-240VAC

We suggest that every light has an independent switch so that you can turn on or turn off the light randomly.

Note: the ground wire (yellow/green double-color wire) must be safely connected, the electrical installation must be in accordance with the related standards

CAUTION: When installing the device, make sure there is no highly inflammable material within a distance of min.5m!

- Connection of Signal Cable

You can use the 3-pin XLR cable to connect the output socket of the master and the input socket of the slave light. Connect the DIGITAL OUT socket of the master and the IN socket of the slave light, then, connect the OUT socket to the IN socket of the next light. Ordinal to connect all the lights as below:

The connection between the output of master and input of product, it’s available to use the 3 pins XLR cable.

Signal cable from the DMX output of the controller to the input of the first master light, and connect to the DMX input of second slave light from the DMX output of the first master light, analogously, till connected all the slave lights, and insert the last connector to the output of the final light. (Notice: the diameter of core of every cable should be 0.5mm at least, double core shelter cable should be used).The signal connecting must use the attached 3 pins XLR cable. Notice, all the internal lead wire of the 3 pins XLR cable should not touch to each other or connect to the connector.

A DMX signal terminator is recommended on the last unit of the chain. DMX terminator is a XLR connector with a 120Ω resistor between the pin 2 and pin 3 of the XLR connector

INSTRUCTIONS

The unit has one input and 2  outputs.

Absolutely electric isolation between input and output.

DMX connector (3pin) for 4 individual channels,

Each DMX output features an independent driver and DATA+ & DATA-  LED  indicator.

We strongly recommend that you take time to read this manual fully before you attempt to use the DMX distributor.

DMX input:  from the DMX controller

DMX output: connect to the DMX receiving device

## CONNECTION

Connector  pin designations shall be as follows: pin1:  signal   common  (shield)

pin2: data (- )

pin3: data (+)

  - Receiver cannot more than 31 units before DMX Distributor .

  - Receiver cannot more than 32 units on one output of the DMX

Distributor.

  - Use a terminator on the last receiver with a 120Ω resistor between the pin 2 and pin 3 of the

XLR connector:

The following points have to be considered during the inspection:

All screws for installing the devices or parts of the device have to be tightly connected and must not be corroded. There must not be any deformations on the housing, glass pane, fixations and installation spots.

The electric power supply cables must not show any damage, material fatigue or sediments. Further instructions depending on the installation spot and usage have to be adhered to by a skilled installer and any safety problems have to be removed.  We recommend a frequent cleaning of the device. Please use a moist, lint-free cloth. Never use alcohol or solvents.

CAUTION: Disconnect from mains before starting maintenance operation!

### Cleaning and Using Frequency of Product

Please make sure that the light is power off before dismantling or maintaining, it’s very important to keep the light clean. Frequent cleaning will ensure maximum brightness output, but also prolong the life time. It’s suggested to use the high quality, professional glass detergent and soft cloth to clean the light. It’s not allowed to use alcohol or chemical solvent. The inner part of the light should be cleaned by vacuum cleaner at least once a year.

When the light doesn’t work, please check if the fuse is burnt out or not. If it is, the same fuse should be replaced, find out the faulty and restart the light. But please note the repair must be handled by professional.

## TECHNICAL SPECIFICATIONS

Fuse (internal): .........................................................................................................F-0.9A/250V PTC

Voltage: ......................................................................................................... AC 110-240V / 50-60Hz

Dimensions:         ………………………………………………………………………..………………………..……100..x110x35mm Weight:         ………………………………………………………………………..………………………………………………...……0.5Kg