# SHOWLIGHT LED STROBE 750

User Manual

At first, thank you for purchasing the device. For the sake of safety and regular operation of this projector, please read this manual carefully before using and operating it in order to avoid any personal injury or damage to the device.

- Packing list：

。。。。。。 a set of device

。。。。。 one user’s guide

- User instruction：

1. After unpacking, please check whether the projector has been damaged by transport such as screw loosening, reflecting mirror broken, etc.

2. Check before electrification. Check whether the projector has been laid correctly

and stably, whether the voltage of the power is adapted to the requirement, otherwise we’ll not be responsible for the damage of the light.

3. This projector is the first class protected equipment. Notice that while using the ground wires have to connect to the earth properly by professionals. Please examine the electrics and voltage before powering on it. Keep sure the supplied voltage stable and required. We suggest customers apply a110v voltage regulator if necessary. It’ll check itself in seconds after being electrified, could be used.

- Technical Parameters:

Rated Voltage：AC220V

Rated Frequency：50Hz

Rated power：250W

Diodes Quantity：8PCS*25W High Brightness LEDS

Channels：5 Channels

Control signal：Standard DMX-512 signal

Function Model:DMX-512 controlled, music controlled, Automatic, Master/slave

Working environment：Indoor use

- Display Panel Operation：

A．Function

E                      B. UP

C．Down

D．Enter

E．LED Display Screen

A    B     C    D
Operation Introduce：After starting press MANU enter into main-menu,，Press UP（on）DOWN（down）to select the submenu, and then press ENTER ensure

- LED Digital display operate

| No. | Display | Function Introduce |
| --- | --- | --- |
| 1 | A001 | 8CHS Address code，（001—512）B、C Up Down address code value |
| 2 | dISP | Display Cis-trans,YES is Cis,SEY is Trans |
| 3 | LOdA | Data RESET ,YES is reset, NO keep original set |
| 4 | S0u1 | Sound1 Strobe Effect (LED not bright) |
| 5 | SOu2 | Sound 2 Strobe Effect (LED Slow strobe) |
| 6 | Au00 | Auto Strobe Effect（000—255）from slow to fast |

3．DMX512Channesl Introduce

| No. | Function | Describe |
| --- | --- | --- |
| CH1 | Dimmer | Dimmer，liner dimming，0-255 from dark to bright |
| CH2 | Strobe | 0-3 Black 4-255 from slow to fast strobe effect |
| CH3 | Running | 0-9 Black 10-255 from slow to fast running light effect |
| CH4 | Explode strobe | 0-9 Black 10-255 Explode strobe effect 2 Second |
| CH5 | Auto | 0-9 Black 0-255 from slow to fast（Strobe，running，Scattered flash alternately） |

- Notice about Master-slave synchronization:

1. When the master machine is running, the light will send DMX-512 signals, however, it can’t be connected to the controller, otherwise, they will interrupt each other , thus that can not be synchronized.

2. While many lights are using master-slave synchronization, only one of them can be master, or they can’t be synchronized.

- The connection of Master-slave synchronization as below:

- Safety Notice:

1. Please make sure to switch off the power before installation or maintenance.

2. Please keep the fan expedite and environment ventilated.

3. This laser projector is designed for the indoor, so while using, please avoid any dripping. If you want to use outdoor, please do enough waterproof measure.

4. Please get acquainted with the properties the light before Installation, operating or maintaining, as most damage are caused by wrong operating without acquaintance.

5. Do not use any power voltage or light type of different specifications.

6.Please do not look at the laser light directly, in case it might damage the eyes.

7. Avoid electric shock！

8. Do not use it frequently under the humid atmosphere.

- Maintenance:

We suggest that clean the light with professional glass cleaning and downy cloth. Keeping the light clean regularly can not only get the largest power of the light.